# TMV7A.EXE SOFTWARE DESIGN SPEC
1.0.0
3 Aug 2013

# General Requirements

1. Within this document, the following terms shall be used to mean:
2. The term “program” shall refer to the TMV7A.EXE program described in this document.
3. The term “Radio” shall refer to the TM-V7A transceiver.
4. The program shall use a standard windows interface (GUI).
5. The program shall use the Kenwood PG-4S programming cable through a standard serial interface, using any available Serial Port.
6. The program shall work with the radio as a remote control head to replace the unusable LED display.
7. The program shall emulate the radio control head as close as possible.
8. The program shall provide the capability to set the radio configuration.
9. The program shall provide the capability to control the radio using both VFO and Memory modes.
10. The program shall maintain all databases locally, not in the radio.
11. The program shall provide a detailed Help file.
12. The program shall provide Context Sensitive Help.
13. The program shall provide the capability to import data files from the Kenwood MCP-V7 radio control program.
14. The program shall provide the capability to import data files from the RCV7 radio control program.
15. The program shall provide the capability to Read, Save and Edit TMV-7 data files.
16. The program shall maintain all program configuration data in a standard Windows .INI file.
17. The program shall automatically load the TMV7 configuration data on startup;
18. The program shall automatically save the TMV7. configuration data on shutdown;
19. The program shall replace the Kenwood “CALL” channel functionality with locally maintained “FAVOURITE” channel functionality;
20. The program shall provide the following radio functionality:
  Band Select;
  VHF and UHF VFO mode;
  VHF and UHF Memory channel configuration;
  VHF and UHF Memory channel selection;
  Power On/Off;
  Favourite channel configuration;
  Favourite channel selection;
  Scan start/stop; and,
  LCD panel display status for the selected channel, including the following indicators:

  PTT	- TX Band selection;
  H, M, L	- RF Power selection;
  DT	- DTSS code functionality;
  T	- PL Tone functionality;
  CT	- CTSS functionality;
  R	- Reverse Frequency functionality
  S, +, -	- Repeater Offset selection;
  =	- Split Memory Channel functionality;
  LOCK	- Transceiver Lock capability;
21. The program shall provide Transceiver Guide functionality;
22. The program shall provide the capability to switch the power on and off;
23. The program shall provide the capability to select the VHF or UHF band;
24. The program shall provide the capability to tune memory channels up or down;
25. The program shall provide the capability to select output power levels of H, M and L on an individual frequency/channel basis;
26. The program shall provide the capability to select a standard repeater offset direction of:
  S	- Simplex;
  +	- Up, or;
  -	- Down;
27. The program shall provide the capability to assign a split offset frequency;
28. The program shall provide the capability to select a Tone frequency from a list of standard frequencies;
29. The program shall provide the capability to activate and de-activate the Tone function;
30. The program shall provide the capability to select the reverse function for all frequencies;
31. The program shall provide the capability to store VHF, UHF and Favourite memory channels;
32. The program shall provide the capability to select VHF, UHF and Favourite memory channels for radio operation;
33. The program shall provide the capability to edit VHF, UHF and Favourite memory channels;
34. The program shall provide the capability to clear VHF, UHF and Favourite memory channels;
35. The program shall provide the capability to name VHF, UHF and Favourite memory channels and UHF and VHF VFO frequencies;
36. The program shall replace the single “CALL” channel function with “FAVOURITE” channel functionality providing up to 12 Favourite channels;
37. The program shall provide “Scan” functionality for VHF, UHF and Favourite memory channels;
38. The program shall provide the capability to “Lockout” VFH, UHF and Favourite channels from the Scan functionality;
39. The program shall provide “”Program Scan” functionality;
40. The program shall provide the capability to enter a CTCSS code from a list of standard frequencies;
41. The program shall provide the capability to activate and de-activate the CTCSS function;
42. The program shall provide the capability to enter a DTSS code of three digits;
43. The program shall provide the capability to activate and de-activate the DTSS function;
44. The program shall provide the capability to enter up to 10 DTMF tones of 1 to 16 values;
45. The program shall provide the capability to edit DTMF entries;
46. The program shall provide the capability to clear DTMF entries;
47. The program shall provide an Automatic Power Off (APO) capability;
48. The program shall provide the capability to “Lock” the transceiver;
49. When the radio is in “Transmit” mode, the program shall display the Transmit frequency;
50. When the radio is in “Transmit” mode, the program shall display the RF output level;
51. When the radio is in “Transmit” mode, the program shall display an “On Air indicator;
52. When the radio is receiving a signal, the program shall display a “Busy” indicator;
53. When the radio is receiving a signal, the program shall display the received signal strength;
54. The program shall make maximum use of colour in the LCD display;
55. The program shall provide the capability to print formatted listings of the following files:
  TMV Data files, and
  .INI Configuration files.
56. The program shall make maximum use of “Hot Keys”;
57. The program shall provide the capability for User Registration with Nag screen;
# INI FILE ENTRIES
### SECTION KEY
CONFIG	Com Port
Colour Scheme
TMV FILES	TMVFileName
UHF	UHF Data Source
UHF Channel Nr
UHF VFO
UHF RX Frequency
UHF Step
UHF Shift
UHF Reverse
UHF Tone
UHF CTCSS
UHF DTSS
UHF Tone Nr
UHF DTSS Code
UHF CTCSS Nr
UHF Offset
UHF Scan
UHF Split Freq
UHF Split Step
UHF RF Power
UHF Channel Name
UHF Comments
UHF Audio Level
UHF Squelch Level
VHF	VHF Data Source
VHF Channel Nr
VHF RX Frequency
VHF Step
VHF Shift
VHF Reverse
VHF Tone
VHF CTCSS
VHF DTSS
VHF Tone Nr
VHF DTSS Code
VHF CTCSS Nr
VHF Offset
VHF Scan
VHF Split Freq
VHF Split Step
VHF RF Power
VHF Channel Name
VHF Comments
VHF Audio Level
VHF Squelch Level

LCD DISPLAY
PTT Band

VHF VFO	VHF VFO
VHF RX Frequency
VHF Step
VHF Shift
VHF Reverse
VHF Tone
VHF CTCSS
VHF DTSS
VHF Tone Freq
VHF DTSS Code
VHF CTCSS Freq
VHF Offset
VHF Scan
VHF RF Power
VHF MEM Name
VHF Comments
UHF VFO	UHF VFO
UHF RX Frequency
UHF Step
UHF Shift
UHF Reverse
UHF Tone
UHF CTCSS
UHF DTSS
UHF Tone Freq
UHF DTSS Code
UHF CTCSS Freq
UHF Offset
UHF Scan
UHF RF Power
UHF MEM Name
UHF Comments

# TMV DATAFILE STRUCTURE
The TMV Data File consists of four header records and a series of comma-delimited entries for each section.
The Sections are [VHF MEMORY], [UHF MEMORY], [FAVOURITES] and [DTMF]. The VHF and UHF MEMORY sections can have from 0 to gv7Max_VHF_Data_Array_Size and gv7Max_UHF_Data_Array_Size records. The Favourites section can have from 0 to gv7Max_Favourites_Data_Array_Size records. The DTMF section can have from 0 to gv7Max_DTMF_Data_Array_Size.
A Default TMV file will start with all fields (null) except for the Channel Nr. Any field with a Channel Name is considered an “active” field and must contain data as detailed in the following table.
# FIELD TYPE DATA FORMAT
VHF, UHF and FAVOURITES Sections
Section_Header	[VHF MEMORY], [UHF MEMORY],
and [FAVOURITES]
ChannelNr	STRING	[1..MaxElementNr] Array Element	[1..gv7Max_VHF_Data_Array_Size ]
VFO	STRING	[UHF, VHF]
RXFrequency	STRING	999.999 (Frequency in mHz)
Step	STRING	(99)9(.9)
Shift	STRING	[S, P, M]
Reverse	STRING	[Off,On]
Tone	STRING	[N, T, C]
ToneFreq	STRING	If Tone = None then field is null
    else (9)99.9
DTSS	STRING	[Off,On]
DTSSCode	STRING	if DTSS = Off then field is null
    else [000..999]
ShiftOffset	STRING	If Shift = S then field is null
    else 99.99
Scan	STRING	[Off,On]
RFPower	STRING	[H, M, L]
ChannelName	STRING	[5..15] Alphanumeric
Comments	STRING	[0..30] Alphanumeric

DTMF Section
Section_Header	[DTMF]
DTMF_Channel	STRING	two digits [.00..09]
DTMF_Code	STRING	16 characters from the sets
    [0..9] and [A..F].
# VHF DATA ARRAY STRUCTURE
The VHF Data array is a string array consisting of up to gv7Max_VHF_Data_Array_Size comma-delimited entries. Formats are defined in the TMV7.EXE Control Protocol document.
# FIELD TYPE DATA FORMAT
VHF_MEM_Channel	STRING	Format 11
VHF_VFO	STRING	Format 3
VHF_RX_Frequency	STRING	11 digits - Freq in kHz
VHF_Step	STRING	Format 6
VHF_Shift	STRING	Format 7
VHF_Reverse	STRING	Format 1
VHF_Tone	STRING	Format 1
VHF_CTCSS	STRING	Format 1
VHF_DTSS	STRING	Format 1
VHF_Tone_Freq	STRING	Format 8
VHF_DTSS_Code	STRING	Format 9
VHF_CTCSS_Freq	STRING	Format 8
VHF_Offset	STRING	Format 10
VHF_Scan	STRING	Format 1
VHF_RF_Power	STRING	Format 12
VHF_MEM_Name	STRING	[5..15] Alphanumeric
VHF_Comments	STRING	[0..30] Alphanumeric

# UHF DATA ARRAY STRUCTURE
The UHF Data array is a string array consisting of up to gv7Max_UHF_Data_Array_Size comma-delimited entries. Formats are defined in the TMV7.EXE Control Protocol document.
# FIELD TYPE DATA FORMAT
UHF_MEM_Channel	STRING	Format 11
UHF_VFO	STRING	Format 3
UHF_RX_Frequency	STRING	11 digits - Freq in kHz
UHF_Step	STRING	Format 6
UHF_Shift	STRING	Format 7
UHF_Reverse	STRING	Format 1
UHF_Tone	STRING	Format 1
UHF_CTCSS	STRING	Format 1
UHF_DTSS	STRING	Format 1
UHF_Tone_Freq	STRING	Format 8
UHF_DTSS_Code	STRING	Format 9
UHF_CTCSS_Freq	STRING	Format 8
UHF_Offset	STRING	Format 10
UHF_Scan	STRING	Format 1
UHF_RF_Power	STRING	Format 12
UHF_MEM_Name	STRING	[5..15] Alphanumeric
UHF_Comments	STRING	[0..30] Alphanumeric

# FAVOURITE DATA ARRAY STRUCTURE
The Favourites Data array is a string array consisting of up to gv7Max_FAV_Data_Array_Size comma-delimited entries. Formats are defined in the TMV7.EXE Control Protocol document.
# FIELD TYPE DATA FORMAT
FAV_MEM_Channel	STRING	Format 11
FAV_VFO	STRING	Format 3
FAV_RX_Frequency	STRING	11 digits - Freq in kHz
FAV_Step	STRING	Format 6
FAV_Shift	STRING	Format 7
FAV_Reverse	STRING	Format 1
FAV_Tone	STRING	Format 1
FAV_CTCSS	STRING	Format 1
FAV_DTSS	STRING	Format 1
FAV_Tone_Freq	STRING	Format 8
FAV_DTSS_Code	STRING	Format 9
FAV_CTCSS_Freq	STRING	Format 8
FAV_Offset	STRING	Format 10
FAV_Scan	STRING	Format 1
FAV_RF_Power	STRING	Format 12
FAV_MEM_Name	STRING	[5..15] Alphanumeric
FAV_Comments	STRING	[0..30] Alphanumeric

# DTMF DATA ARRAY STRUCTURE
The DTMF Data array is a string array consisting of up to gv7Max_DTMF_Data_Array_Size comma-delimited entries
# FIELD TYPE DATA FORMAT
DTMF_Channel	STRING	Format 15
DTMF_Code	STRING	Format 16.

# VFO DATA ARRAY STRUCTURES
The VFO Data arrays are identical string arrays with data elements prefixed by VHF or UHF
# FIELD TYPE DATA
  RXFrequency	STRING	Format 5
  Step	STRING	Format 6
  Shift	STRING	Format 7
  Reverse	STRING	Format 1
  Tone	STRING	Format 1
  CTCSS	STRING	Format 1
  DTSS	STRING	Format 1
  ToneNr	STRING	Format 8
  DTSSCode	STRING	Format 9
  CTCSSNr	STRING	Format 8
  Offset	STRING	Nine digits – Freq in Hz
  Scan	STRING	Format 1
  SplitFrequency	STRING	Format 10
  SplitStep	STRING	Format 6
  RFPower	STRING	Format 12
  ChannelName	STRING	[5..15] Alphanumeric
  ChannelComments	STRINF	[0..30] Alphanumeric
  AudioLevel	STRING	Format 19
  SquelchLevel	STRING	Format 20